COUNTY OF CLEVELAND, NORTH CAROLINA

PURCHASING DEPARTMENT

DATE: MAY 5, 2006

REQUEST FOR BIDS AND PROPOSALS

ARTICULATED DUMP TRUCK

PURSUANT TO GENERAL STATUTES OF NORTH CAROLINA, SECTION 143-129, AS AMENDED, SEALED BIDS AND PROPOSALS ARE INVITED AND SUBJECT TO THE CONDITIONS AND SPECIFICATIONS HEREIN, WILL BE RECEIVED AT THE OFFICE OF THE CLEVELAND COUNTY PURCHASING AGENT UNTIL 10:00 O’CLOCK am FRIDAY, JUNE 16, 2006, AT WHICH TIME A MEETING AT THE COUNTY ADMINISTRATION BUILDING, 311 E MARION STREET, SHELBY, NC. THE SEALED BIDS AND PROPOSALS WILL BE PUBLICLY OPENED FOR FURNISHING THE, EQUIPMENT AS DESCRIBED BELOW.

THE COUNTY OF CLEVELAND, NC

BY: Kim Ogle (704) 484-4840

## PURCHASING AGENT

## ITEM NO.					DESCRIPTION

1.	Please read carefully the Terms and Conditions.

2.	Cleveland County will need to purchase a Used 2002 or Newer Articulated Dump Truck.

3.	No Bid Bond required on this purchase.

4.	No Performance Bond required on this purchase.

5.	Should you have any questions regarding this bid contact Jack Brack at (704) 482–9061 or myself at the above number.

6.	Cleveland County reserves the right to purchase additional Equipment for a twelve (12) month period from the contract date at the original pricing.

CONDITIONS

- ALL BIDS AND PROPOSALS SHALL BE FOR FURNISHING APPARATUS, SUPPLIES, MATERIALS, EQUIPMENT AND/OR WORK AND SERVICES IN ACCORDANCE WITH THE APPLICABLE PLANS AND SPECIFICATIONS PRESCRIBED BY CLEVELAND COUNTY. FROM THE DATE SHOWN UNTIL THE DATE OF OPENING THE PROPOSALS, THE PLANS AND SPECIFICATIONS OF THE PROPOSED WORK AND/OR A COMPLETE DESCRIPTION OF THE APPARATUS, SUPPLIES, MATERIALS, EQUIPMENT AND/OR WORK AND SERVICES ARE AND WILL CONTINUE TO BE ON FILE IN THE OFFICE OF THE PURCHASING AGENT FOR CLEVELAND COUNTY DURING USUAL OFFICE HOURS AND AVAILABLE TO PROSPECTIVE BIDDERS.

- THE COUNTY RESERVES THE RIGHT TO EVALUATE ALL BIDS ESPECIALLY WHERE THERE IS A WIDE RANGE IN SPECIFICATIONS OR TO REJECT ANY AND ALL BIDS AND PROPOSALS, AND FURTHER SPECIFICALLY RESERVES THE RIGHT TO MAKE AWARD AND/OR AWARDS IN THE BEST INTEREST OF CLEVELAND COUNTY.

- TIME, IN CONNECTION WITH DISCOUNT OFFERED WILL BE COMPUTED FROM DATE OR DELIVERY OF THE SUPPLIES OR MATERIALS ON DELIVERY AT DESTINATION WHEN FINAL INSPECTION AND ACCEPTANCE ARE THOSE POINTS OR FROM DATE CORRECT INVOICE IS RECEIVED IF LATTER IS LATER THAN THE DATE OF DELIVERY GUARANTEED MAXIMUM PRICE MUST BE SHOWN IN ALL BIDS.

- THE BIDDER AND/OR BIDDERS TO WHOM CONTRACT IS AWARDED MUST COMPLY FULLY WITH THE REQUIREMENTS OF GENERAL STATUTES SECTION 143-129 AS AMENDED, INCLUDING ENTERING INTO A COUNTY-PREPARED CONTRACT AND THE FURNISHING OF A SATISFACTORY SURETY BOND IN THE FULL AMOUNT OF THE CONTRACT PRICE TO GUARANTEE FAITHFUL PERFORMANCE OF THE CONTRACT.

- IN CASE OF DEFAULT OF THE CONTRACTOR THE COUNTY MAY PROCURE THE ARTICLES OR SERVICES FROM OTHER SOURCES AND HOLD THE CONTRACTOR RESPONSIBLE FOR ANY EXCESS COST OCCASIONED THEREBY.

- PAYMENT BY THE COUNTY DUE THIRTY DAYS AFTER DELIVERY AND INSPECTION BY THE USER AGENCY UNLESS OTHERWISE SPECIFICALLY PROVIDED; SUBJECT TO ANY DISCOUNTS ALLOWED.

- THE COUNTY MAY AT ITS OPTION PURCHASE ADDITIONAL ITEMS UNDER THE TERMS AND AT THE SAME PRICES CONTAINED IN THE CONTRACT BY EXTENDING SUCH CONTRACT FOR ADDITIONAL ANNUAL PERIODS NOT TO EXCEED FOUR IN NUMBER PROVIDED; IF THE VENDOR CAN SATISFACTORILY ILLUSTRATE TO THE COUNTY THAT ITS COST OF MATERIALS OR LABOR INCREASED SIGNIFICANTLY THE VENDOR MAY DECLINE THE OPTION FOR ANY SUCH CONTRACT EXTENSION.

- BIDS MUST BE RETURNED IN ITS ENTIRETY. BIDS RECEIVED BY THE COUNTY INCOMPLETE MAY BE CONSIDERED INVALID AND REJECTED ON THESE GROUNDS.

- THE SPECIFIED ITEM(S) SHALL BE DELIVERED F.O.B. TO SHELBY, NC ACCORDING TO THE ADDRESS STATED ON THE PURCHASE ORDER UNLESS STATED OTHERWISE IN THE SPECIAL CONDITIONS.

# INSTRUCTIONS TO BIDDERS

- SAMPLES OF ITEMS, WHEN REQUIRED MUST BE FURNISHED FREE OF EXPENSE, PRIOR TO THE OPENING OF BIDS AND IF NOT DESTROYED WILL UPON REQUEST, BE RETURNED AT THE BIDDERS EXPENSE. REQUEST FOR THE RETURN OF SAMPLES MUST BE MADE WITHIN 10 DAYS, FOLLOWING OPENING OF BIDS. EACH INDIVIDUAL SAMPLE MUST BE LABELED AND ITEM NUMBER.

- PRICES SHOULD BE STATED IN UNITS OF QUANTITY SPECIFIED WITH PACKING INCLUDED.

- IF THE ITEM BID UPON HAS A TRADE NAME OR BRAND SUCH TRADE NAME OR BRAND MUST BE STATED IN THE BID.

- ATTACH COMPLETE SPECIFICATIONS FOR ANY SUBSTITUTION OFFERED OR WHEN AMPLIFICATION IS DESIRABLE OR NECESSARY.

- IF DESCRIPTIVE MATTER IS ATTACHED TO BID, BIDDER’S NAME MUST BE ON SHEET CONTAINING DESCRIPTIVE MATTER.

- WHERE A BRAND OR TRADE NAME APPEARS IN THE SPECIFICATIONS IT IS UNDERSTOOD THAT IT REFERS TO THAT MATERIAL OR IT’S EQUIVALENT.

- PLEASE ADDRESS AND MARK YOU BID AS SHOWN BELOW.

Proposal Page

Used Articulating Dump Truck 2002 or Newer Model

with no more than 4000 hours

and a minimum (3) three year power train warranty

meeting all specifications as outlined.

Unit Price		Extended Price

Articulating Dump Truck						         $			                       $

Year                                    __________________________________

Manufacturer

Model                                 __________________________________

Hours                                 ___________________________________

Warranty                            ___________________________________

Delivery Cost											         $

Total Cost											         $

Sales Tax											         $

Delivery in		 days

The undersigned certifies that the equipment they are proposing for this project meets or exceeds the minimum specifications as listed in this bid package.

Company Name						  	 Company Address

Company Officer/Title					  	 Officer Signature

Federal Tax ID#						   Telephone #

Date

CLEVELAND COUNTY

SPECIFICATION FOR ARTICULATED DUMP TRUCK

25 TON / 18 YARD SIZE CLASS

USED 2002 OR NEWER

GENERAL:

The purpose and intent of these specifications is to describe a heavy duty, diesel powered Articulated Dump Truck suitable for work with Cleveland County Landfill.  The truck shall be the latest standard new production model at the time of delivery.  The truck must be the same as normally supplied to the construction industry and shall conform to all specifications listed below.  All parts and attachments not specifically listed, but which are necessary to furnish a complete ready-to-work unit, shall be provided.  All manufacturers’ standard equipment for model quoted shall be provided.  The truck shall meet all Federal and State safety standards in force at time of delivery.

ENGINE:

Minimum 6-cylinder diesel, direct start, direct injection, turbo-charged four-cycle diesel with a minimum of 265 net flywheel HP.  Unit shall have keyed electric starter.

TRANSMISSION:

Transmission shall be power shift, torque converter type. Transmission shall have at least 6 forward and 1 reverse speeds and equipped with automatic shift between gears and automatic lock-up to direct drive.  Sight gauge or dip stick for transmission and hydraulic fluid level.

AXLES:

Unit shall have six wheel drive and heavy-duty type axles with planetary final drive.  Front and rear axles shall have limited slip in all axles.  Truck shall have inter-axle differential with operator controllable lock.

STEERING:

Power steering with articulation and oscillation joint.

TIRES:

Minimum of 23.5R25 radial tires.

BRAKES:

Six-wheel air over hydraulic or hydraulic only operation with disc type brakes.  Separate automatically applied parking brake (when hydraulic or air pressure falls) with warning light on dash.

ELECTRICAL SYSTEM:

Twelve or twenty four volt system with minimum of 60 amp alternator.  Unit shall have front headlights with guards and front and rear work lights with guards mounted on top of cab. Flashing warning lights and turn signal lights with guards. 8 inch revolving light mounted on top of cab.  Master electrical disconnect. Backup alarm with horn that can be heard over the unit noise. Full set of gauges and/or monitoring system to include tachometer, hourmeter and speedometer. Dual batteries with minimum of 900 CCA rating each and master electric disconnect switch.

BASIC OPERATING WEIGHT:

Machine to weigh a minimum of 35,000 pounds. Truck to be rated to haul 50,000 pounds with a minimum of 18 yd. heaped truck body.

CAB:

Safety ROPS cab, enclosed with tinted safety glass and key locked door. Cab to have full coverage outside rear view mirrors, front wiper with washer. Factory air conditioning installed. Heater and defroster fan. Adjustable deluxe suspension seat with seat belt.

GENERAL:

Truck to have front and rear tow hitch.  Truck shall have either automatic exhaust brake or automatic transmission retarder.  Truck to have full rear tailgate to allow county to haul muck.

WARRANTY:

The bidder shall provide a (3) three-year power train full coverage warranty in bid. Bidder must include copy of warranty with bid package.

MISCELLANEOUS:

Bidder to supply two copies of operators’ manuals, maintenance manuals, service manuals and parts manuals with unit at time of delivery.  The Bidder to provide qualified instruction to the County operators and mechanics at time of delivery on the operation and maintenance of the unit.  Unit shall be delivered to Cleveland County Landfill in Shelby, North Carolina, complete and ready to work.

PARTS AVAILABILTY GUARANTEE:

During the 5 year 7500 period the bidder shall guarantee parts delivery within 48 hours of being ordered or the part will be provided at no cost to Cleveland County.  If the truck is down for more than 48 hours through no fault of Cleveland County the vendor shall provide the county a comparable truck at no cost to the county while their machine is down.  Vendor shall provide a complete list of exceptions of the minimum specifications in the space provided below.  Bids not meeting the minimum specifications shall not be considered.

## EXCEPTIONS:

## Bidder to state all exceptions to bid specification and attach a copy of current literature on unit bid.  County reserves the right to require an on site demonstration of the unit as bid to County before award of bid.

# Text boxes

CLEVELAND COUNTY PURCHASING DEPARTMENT

311 E. MARION ST. (or) PO BOX 1210

SHELBY, NC 28151

BID REQUEST FOR:  Used Articulated Dump Truck

TO BE OPENED	   10:00		O’CLOCK		AM

DATE		FRIDAY		   JUNE 16, 2006